## Slide 1: References
Donald A Neamen, Electronic Circuits-Analysis and Design Text book
Sedra and Smith, Microelectronics Text book (some portion).
Raza Vi, Fundamentals of Microelectronics, Reference book
Milliman and Halikas, Microelectronics, Reference book

## Slide 2: BJT: Bipolar Junction Transistor
Discuss the physical structure and operation of the bipolar junction transistor.
Understand the dc analysis and design techniques of bipolar transistor circuits.
Investigate various dc biasing schemes of bipolar transistor circuits, including integrated circuit biasing.

## Slide 3
Base is very narrow
  Emitter ~ 1019 /cm3
  Base ~ 1017 /cm3
  Collector ~ 1015 /cm3
Electrically unsymmetrical
Four biasing conditions
  Depending on forward or reverse bias

## Slide 4: Cross Section of Integrated Circuit npn Transistor
Complex structure

## Slide 5: Modes of Operation
Forward-Active
  B-E junction is forward biased
  B-C junction is reverse biased
Saturation
  B-E and B-C junctions are forward biased
Cut-Off
  B-E and B-C junctions are reverse biased
Inverse-Active (or Reverse-Active)
  B-E junction is reverse biased
  B-C junction is forward biased

## Slide 6: npn BJT in Forward-Active

## Slide 7: Understanding the current flow in npn transistor
Emitter current
Depends on cross-section (10-12 -10-15 A)
Due to large concentration gradient, electrons injected from emitter diffuse across the base in to B-C space region where EF sweeps them into collector, forming collector current which depends on the B-E voltage
Collector current

## Slide 8
ic <iE ; ic = a iE , where a is called as common base current gain and is less than unity.
Base Current:
  Two components
    Flow of holes
    Recombination with majority carriers (recombination current)

## Slide 9: Electrons and Holes in pnp BJT

## Slide 10
npn
pnp

## Slide 11
Collector
Base
Emitter
Movement of electrons and holes in npn transistor

## Slide 12: Circuit Symbols and Current Conventions

## Slide 13: Common emitter current gain
Defined as ratio of collector and base current
Key parameter
  Assumed as constant for any given transistor
    50<b<300
    Highly dependent on fabrication

## Slide 14: Current Relationships

## Slide 15: Common-Emitter Configurations
True for active region only

## Slide 16: Common-Base Configuration
Current source provide emitter current

## Slide 17: Current-Voltage Characteristics of a Common-Base Circuit
B-C/C-B junction forward biased, transistor no longer in forward active mode
B-C/C-B, reverse biased, ic ~ iE
common-base: ideal constant current-source

## Slide 18: Current-Voltage Characteristics of a Common-Emitter Circuit
VCE ≥ VBE (on)
Finite slope to the curves
-due to base-width modulation
- observed by J.M. Early
- called as Early effect

## Slide 19
Common-base
Common-emitter

## Slide 20: Early Voltage/Finite Output Resistance

## Slide 21: DC analysis of transistor circuits
Use of piecewise linear model of pn junction
Assume transistor in forward active mode
Common emitter configuration
VCE>VBE (on)

## Slide 22: DC Equivalent Circuit for npn Common Emitter

## Slide 23
Example 1.

## Slide 24: DC Equivalent Circuit for pnp Common Emitter

## Slide 25: Load Line
Helps to visualize the characteristics of a transistor circuit

## Slide 26: Saturation mode
VBB IB Q-point
As base current continue to increase, a point is reached where the collector current IC can no longer increase.
- Transistor is biased in saturation mode
IC/IB < b

## Slide 27
Example 2:
circuit
Circuit showing values with an assumption of forward active mode
Circuit showing values with an assumption of saturation mode

## Slide 29: Problem-Solving Technique: Bipolar DC Analysis
Assume that the transistor is biased in forward active mode
  VBE = VBE(on), IB > 0, & IC = bIB
Analyze ‘linear’ circuit.
Evaluate the resulting state of transistor.
  If VCE > VCE(sat), assumption is correct
  If IB < 0, transistor likely in cutoff
  If VCE < 0, transistor likely in saturation
If initial assumption is incorrect, make new assumption and return to Step 2.

## Slide 30: Voltage Transfer Characteristic for npn Circuit

## Slide 31: Voltage Transfer Characteristic for pnp Circuit

## Slide 32: BJT Biasing
Single base resistor biasing
Voltage divider biasing
  Biasing stability

## Slide 33: Single Base Resistor Biasing

## Slide 35: Common Emitter with Voltage Divider Biasing and Emitter Resistor
RB is replaced by R1 and R2.
Emitter resistor is added. AC signal is coupled through Cc.
Analyzed by Thevenin equivalent circuit for the base circuit.
(1)

## Slide 36
Use of KVL in B-E loop
If the transistor is biased in forward-active mode
(2)
(3)
From (2), the base current can be calculated. Hence, the collector current can be found
The design requirement for bias stability is
The collector current is therefore,

## Slide 37
b >> 1, b/(1+b) ~ 1

## Slide 38
Example:

## Slide 39: BJT Amplifier
Two types analysis
  DC analysis
    Applied DC voltage source
  AC analysis
    Time varying signal source
Superposition principle (linear amplifier)
  The response of a linear amplifier circuit excited by multiple independent input signals is the sum of the responses of the circuit to each of the input signals alone.

## Slide 40: Bipolar linear amplifier
Variable | Meaning
iB, vBE | Total instantaneous values
IB, VBE | DC values
ib,vbe | Instantaneous ac values
Ib, Vbe | Phasor values

## Slide 41: Common Emitter with Time-Varying Input

## Slide 42: IB versus VBE Characteristic

## Slide 43
Total Harmonic Distortion (THD)

## Slide 44: ac Equivalent Circuit for Common Emitter

## Slide 45: Small-Signal Hybrid p Model for npn BJT
Phasor signals are shown in parentheses.

## Slide 46: Small-Signal Equivalent Circuit Using Common-Emitter Current Gain

## Slide 47: Small-Signal Equivalent Circuit for npn Common Emitter circuit-voltage gain

## Slide 48: Problem-Solving Technique: BJT AC Analysis
Analyze circuit with only dc sources to find Q point.
Replace each element in circuit with small-signal model, including the hybrid p model for the transistor.
Analyze the small-signal equivalent circuit after setting dc source components to zero.

## Slide 49
Calculate the small-signal voltage gain of the BJT as shown in figure. Assume the transistor and circuit parameters are b = 100, VCC =12 V, VBE = 0.7 V, RC = 6 k , RB = 50 k, and VBB =1.2 V.

## Slide 50: Hybrid p Model for npn with Early Effect

## Slide 51: Hybrid p Model for pnp with Early Effect

## Slide 52: BJT Amplifier configurations
Common emitter
  Basic common emitter amplifier
  With Emitter resistor
  With bypass capacitor
Common collector (emitter follower)
Common base

## Slide 53: 4 Equivalent 2-port Networks
Voltage Amplifier
Current Amplifier

## Slide 54
4 Equivalent 2-port Networks
Transconductance Amplifier
Transresistance Amplifier

## Slide 55: Common Emitter with Voltage-Divider Bias and a Coupling Capacitor

## Slide 56: Small-Signal Equivalent Circuit – Coupling Capacitor Assumed a Short

## Slide 57: npn Common Emitter with Emitter Resistor

## Slide 58: Small-Signal Equivalent Circuit: Common Emitter with RE

## Slide 59: RE and Emitter Bypass Capacitor

## Slide 60: Field Effect Transistors (FET)
Metal-Oxide Semiconductor FET (MOSFET)
  n-type MOS
  p-type MOS
Junction FET (JFET)
  pn junction FET

## Slide 61: MOSFET
Basic MOS capacitor structure
Smaller in size
High density VLSI
Based on field enhancement
Modulation of conductance of semiconductor substrate

## Slide 62: p-type
Understanding the field enhancement

## Slide 63: n-type
p-type substrate: +ve gate voltage
n-type substrate: -ve gate voltage

## Slide 64: n-channel enhancement mode MOSFET
Channel length, L ~ 1 mm
Oxide length, tox ~ 400 Angstrom
NMOS (carriers are electrons)
p-type substrate, two n-regions (n-source, n-drain)
Positive Gate voltage

## Slide 65: Basic transistor operation
Cross-section of n-channel MOSFET prior to formation of electron inversion layer
Cross-section after the
formation of electron inversion layer

## Slide 66
Threshold voltage VTN: applied gate voltage required to create an inversion charge in which the density is equal to the concentration of majority carriers in semiconductor substrate.
voltage at which the device turns ON
VGS < VTN, No current
VGS < VTN, current flow (drain to source)
Gate and drain voltages are measured with respect to source

## Slide 67
Thickness of inversion layer gives the relative charge density
VDS increases, the voltage drop across the oxide near the drain terminal decreases
  Decrease in induced charge density
  Decrease in incremental conductance

## Slide 68
VDS increases to a point where the potential difference between gate and drain terminals (VGS-VDS) becomes equal to the threshold voltage
  Induced charge density at drain terminal becomes zero
  Incremental conductance subsequently zero
VGS-VDS(sat)=VTN
VDS(sat)=VGS-VTN

## Slide 69
Family of curves
Ideal current-voltage characteristics

## Slide 70: PMOS
n-type substrate, two p-regions (p-source, p-drain)
Gate voltage ???, carriers ??

## Slide 71
NMOS
PMOS
Circuit symbols

## Slide 73: NMOS Common-Source Circuit
Variable | Symbol meaning
iD,vGS | Total instantaneous values
ID,VGS | DC values
id,vgs | Instantaneous ac values
Id,Vgs | Phasor values

## Slide 74: NMOS Transistor Small-Signal Parameters
Values depends on Q-point
Transconductance (relates output current to input voltage)
-can think as gain of a transistor

## Slide 75: Simple NMOS Small-Signal Equivalent Circuit

## Slide 76: NMOS Common-Source Circuit
AC
Small-signal

## Slide 77: Problem-Solving Technique: MOSFET AC Analysis
Analyze circuit with only the dc sources to find quiescent solution. Transistor must be biased in saturation region for linear amplifier.
Replace elements with small-signal model.
Analyze small-signal equivalent circuit, setting dc sources to zero, to produce the circuit to the time-varying input signals only.

## Slide 78
MOSFET Amplifier Configurations
Common source
Common drain (source follower)
Common gate
Input and output resistance characteristics are important in determining loading effects

## Slide 79: Common-Source Configuration
DC analysis:
Coupling capacitor is assumed to be open.
AC analysis:
Coupling capacitor is assumed to be a short. DC voltage supply is set to zero volts.

## Slide 80: Small-Signal Equivalent Circuit
Output resistance can be calculated by setting the independent input source Vi =0 i.e. Vgs =0.

## Slide 81: DC Load Line
Q-point near the middle of the saturation region for maximum symmetrical output voltage swing,.
Small AC input signal for output response to be linear.

## Slide 82: Example
Determine the small-signal voltage gain and input and output resistances of a common –source amplifier. For the circuit, the parameters are: VDD =10 V, R1=70.9 k, R2=29.1 k, and RD=5 k. The transistor parameters are VTN = 1.5 V, Kn=0.5 mA/V2, and l =0.01 V-1. Assume Rsi= 4 k.

## Slide 83: Common-Source Amplifier with Source Resistor
Source resistor is used to stabilize the Q-point against transistor parameter variation
- decreases the gain
Av = -5.76
Determine the small-signal voltage gain of a common-source circuit containing a source resistor. The transistor parameters are VTN = 0.8 V, Kn= 1 mA/V2, and l =0.

## Slide 84: Small-Signal Equivalent Circuit for Common-Source with Source Resistor
Use of KVL from input around the gate-source loop
If gm is very large,

## Slide 85: Common-Source Amplifier with Bypass Capacitor
Small-signal equivalent circuit
To minimize the loss in small-signal voltage gain as in previous example, while maintaining the Q-point stability, a bypass capacitor can be added, or replacing the source resistor by a constant current source.

## Slide 86
Determine the small-signal voltage gain of a common-source circuit biased with a constant current source and incorporating a source bypass capacitor. The transistor parameters are VTN = 0.8 V, Kn= 1 mA/V2, and l =0.

## Slide 87: Op-Amp
Amplifies the difference between two input signals to give an output signal
20-50 transistors
Ideal op-amp equivalent circuit

## Slide 88: Op-Amp
Ideal
Inverting
Non-inverting
Applications
T-network
Effect of finite gain
Summing amplifier
voltage follower
current to voltage converter
voltage-to-current converter
difference amplifier
integrator & differentiator
precision half-wave rectifier

## Slide 89: Small-Signal Equivalent Circuit: MOSFET with Input and Output Feedback

## Slide 90: Equivalent Circuit of Op-Amp
Output voltage is limited: biased by dc voltages V+ and V-
vo  V+, it will saturate or limited to a value nearly equal to V+, similar for V-.
V- + DV <vo <V+-DV

## Slide 91: Inverting Op-Amp
Equivalent circuit

## Slide 92: Inverting Op-Amp with T-Network

## Slide 93: Inverting Op-Amp with Finite Differential-Mode Gain

## Slide 94
= 3V
60 k
500 
H(f) =j 2pf

Y(t)
X(t)
~
vi
vo
+
-